## Slide 1
薛智文
cwhsueh@csie.ntu.edu.tw
http://www.csie.ntu.edu.tw/~cwhsueh/
2017 Spring
Operating Systems
Wed 234, DTH 102

## Slide 3
百分數 | 等第 | 定義
90-100(95) | A+ | All goals achieved beyond expectation 所有目標皆達成且超越期望
85-89(87) | A | All goals achieved 所有目標皆達成
80-84(82) | A- | All goals achieved, but need some polish 所有目標皆達成，但需一些精進
77-79(78) | B+ | Some goals well achieved 達成部分目標，且品質佳
73-76(75) | B | Some goals adequately achieved 達成部分目標，但品質普通
70-72(71) | B- | Some goals achieved with minor flaws 達成部分目標，但有些缺失
67-69(68) | C+ | Minimum goals achieved 達成最低目標
63-66(65) | C | Minimum goals achieved with minor flaws 達成最低目標，但有些缺失
60-62(61) | C- | Minimum goals achieved with major flaws 達成最低目標但有重大缺失
<59(含) | F | No goals achieved 所有目標皆未達成

## Slide 4: Course Expectation
Understand the OS concepts
Participation
  Ask and answer questions
  Do not skip the class unless …
Team Work
Software Engineering
Turn in projects in time (minimum)

## Slide 6: Chapter 1: Introduction

## Slide 7: Objectives
To provide a grand tour of the major operating systems components
To provide coverage of basic computer system organization

## Slide 8: Chapter 1: Introduction
What Operating Systems Do
Computer-System Organization
Computer-System Architecture
Operating-System Structure
Operating-System Operations
Process Management
Memory Management
Storage Management
Protection and Security
Kernel Data Structure
Computing Environments
Open-Source Operating Systems

## Slide 9: Chapter 1: Introduction
What Operating Systems Do
Computer-System Organization
Computer-System Architecture
Operating-System Structure
Operating-System Operations
Process Management
Memory Management
Storage Management
Protection and Security
Kernel Data Structure
Computing Environments
Open-Source Operating Systems

## Slide 10: What is an Operating System?
A (system) program that
  manages the computer hardware (and software)
  provides a basis for application programs and acts as an intermediary between a user of a computer and the computer hardware.
讓使用者妥善地使用軟硬體資源的系統程式

## Slide 11: Operating System Goals
Mainframe OSes are designed primarily to optimize utilization of hardware.
PC OSes support complex games, business applications, and everything in between.
OSes for handheld systems are designed to provide an environment in which a user can easily interface with the computer to execute programs.
Convenient (GUI), efficient, both, or between.

## Slide 12: Computer System Structure and Components
Similar to
a Government!
Notes: Computer system can be divided into four components
  Hardware – provides basic computing resources
    CPU, memory, I/O devices
  Operating system
    Controls and coordinates use of hardware among various applications and users
  Application programs – define the ways in which the system resources are used to solve the computing problems of the users
    Word processors, compilers, web browsers, database systems, video games
  Users
    People, machines, other computers

## Slide 13: Operating System Definition (1/2)
User View
  Server, Mainframe, Workstations, PC, Handhelds.
System View
  OS is a resource allocator
    Manages all resources
    Decides between conflicting requests for efficient and fair resource use
  OS is a control program
    Controls execution of programs to prevent errors and improper use of the computer

## Slide 14: Operating System Definition (2/2)
No universally accepted definition
“Everything a vendor ships when you order an operating system” is good approximation
  But varies wildly
“The one program running at all times on the computer” is the kernel. Everything else is either a system program (ships with the operating system) or an application program

## Slide 15: 作業系統特徵遷移示意圖
編譯器 無軟體
交談式
網路 多處理器
無軟體 編譯器
分時 多使用者 多處理器
常駐監控常式 網路 容錯
叢集
UNIX
無軟體 編譯器 分時 多使用者 分散式系統
批次 多處理器
常駐監控常式 網路 容錯
UNIX
1950 1960 1970 1980 1990 2000 2010
MULTICS
大型電腦
迷你電腦
個人電腦
無軟體 編譯器
交談式 多處理器
多使用者
網路
UNIX
手持式電腦
虛擬機器
虛擬化
virtualization
虛擬機器
虛擬機器
虛擬機器
Cloud OS?
虛擬化
virtualization
虛擬化
virtualization
WeOS?

## Slide 16: Chapter 1: Introduction
What Operating Systems Do
Computer-System Organization
Computer-System Architecture
Operating-System Structure
Operating-System Operations
Process Management
Memory Management
Storage Management
Protection and Security
Kernel Data Structure
Computing Environments
Open-Source Operating Systems

## Slide 17: Computer System Organization

## Slide 18: Computer-System Operation (1/2)
Computer Startup
  bootstrap program is loaded at power-up or reboot
    Typically stored in ROM or EPROM, generally known as firmware
    Initializates all aspects of system
    Loads operating system kernel and starts execution
One or more CPUs, device controllers connect through common bus providing access to shared memory
Concurrent execution of CPUs and devices competing for memory cycles

## Slide 19: Computer-System Operation (2/2)
I/O devices and the CPU can execute concurrently.
Each device controller is in charge of a particular device type.
Each device controller has a local buffer.
CPU moves data from/to main memory to/from local buffers
I/O is from the device to local buffer of controller.
Device controller informs CPU that it has finished its operation by causing an interrupt.

## Slide 20: How a Modern Computer System Works?
Thread of execution
CPU (*N)
Cache
instructions
and data
memory
device
(*M)
DMA
data movement
instruction execution cycle
I/O request
data
interrupt

## Slide 21: Common Functions of Interrupts
Interrupt transfers control to the interrupt service routine generally, through the interrupt vector, which contains the addresses of all the service routines.
Interrupt architecture must save the address of the interrupted instruction.
Incoming interrupts are disabled while another interrupt is being processed to prevent a lost interrupt.
A trap is a software-generated interrupt caused either by an error or a user request.
An operating system is interrupt driven.

## Slide 22: Interrupt Handling
The operating system preserves the state of the CPU by storing registers and the program counter.
Determines which type of interrupt has occurred:
  polling
  vectored interrupt system
Separate segments of code determine what action should be taken for each type of interrupt

## Slide 23: Interrupt Timeline

## Slide 24: I/O Structure
After I/O starts, control returns to user program only upon I/O completion.
  Wait instruction idles the CPU until the next interrupt
  Wait loop (contention for memory access).
  At most one I/O request is outstanding at a time, no simultaneous I/O processing.
After I/O starts, control returns to user program without waiting for I/O completion.
  System call – request to the operating system to allow user to wait for I/O completion.
  Device-status table contains entry for each I/O device indicating its type, address, and state.
  OS indexes into I/O device table to determine device status and to modify table entry to include interrupt.

## Slide 25: Two I/O Methods
Synchronous
Asynchronous

## Slide 26: Device-Status Table

## Slide 27: Direct Memory Access Structure
Used for high-speed I/O devices able to transmit information at close to memory speeds.
Device controller transfers blocks of data from buffer storage directly to main memory without CPU intervention.
Only one interrupt is generated per block, rather than the one interrupt per byte.

## Slide 28: Storage Structure
Main memory – only large storage media that the CPU can access directly.
Secondary storage – extension of main memory that provides large nonvolatile storage capacity.
Magnetic disks – rigid metal or glass platters covered with magnetic recording material
  Disk surface is logically divided into tracks, which are subdivided into sectors.
  The disk controller determines the logical interaction between the device and the computer.

## Slide 29: Storage Hierarchy
Storage systems organized in hierarchy.
  Speed
  Cost
  Volatility
Caching – copying information into faster storage system; main memory can be viewed as a last cache for secondary storage.

## Slide 30: Storage-Device Hierarchy

## Slide 31: Caching
Important principle, performed at many levels in a computer (in hardware, OS, software)
Information in use copied from slower to faster storage temporarily
Faster storage (cache) checked first to determine if information is there
  If it is, information used directly from the cache (fast)
  If not, data copied to cache and used there
Cache smaller than storage being cached
  Cache management important design problem
  Cache size and replacement policy

## Slide 32: Performance of Various Levels of Storage
Movement between levels of storage hierarchy can be explicit or implicit

## Slide 33: Migration of Integer A from Disk to Register
Multitasking environments must be careful to use most recent value, no matter where it is stored in the storage hierarchy Multiprocessor environment must provide cache coherency in hardware such that all CPUs have the most recent value in their cache
Distributed environment situation even more complex
  Several copies of a datum can exist
  Various solutions covered in Chapter 17

## Slide 34: Chapter 1: Introduction
What Operating Systems Do
Computer-System Organization
Computer-System Architecture
Operating-System Structure
Operating-System Operations
Process Management
Memory Management
Storage Management
Protection and Security
Kernel Data Structure
Computing Environments
Open-Source Operating Systems

## Slide 35: Computer-System Architecture
Single-processor systems
Multiprocessor systems
  Increased throughput
  Economy of scale
  Increased reliability
Clustered systems

## Slide 36: Multiprocessor systems
Graceful degradation
Fault tolerant
Asymmetric multiprocessing
vs. symmetric multiprocessing (SMP)
UMA vs. NUMA
Multicore
Blade server
registers
CPU0
cache
registers
CPU2
cache
registers
CPU1
cache
memory
registers
CPU core0
cache
registers
CPU core1
cache
memory

## Slide 37: Clustered systems
Linked via LAN
Provide high availability
  Hot-standby more
Provide high-performance computing
  Parallelization
Distributed lock manager (DLM)
computer
computer
computer
interconnected
interconnected
Storage Area Network

## Slide 38: Chapter 1: Introduction
What Operating Systems Do
Computer-System Organization
Computer-System Architecture
Operating-System Structure
Operating-System Operations
Process Management
Memory Management
Storage Management
Protection and Security
Kernel Data Structure
Computing Environments
Open-Source Operating Systems

## Slide 39: Operating System Structure
Multiprogramming needed for efficiency
  Single user cannot keep CPU and I/O devices busy at all times
  Multiprogramming organizes jobs (code and data) so CPU always has one to execute
  A subset of total jobs in system is kept in memory
  One job selected and run via job scheduling
  When it has to wait (for I/O for example), OS switches to another job
Timesharing (multitasking) is logical extension in which CPU switches jobs so frequently that users can interact with each job while it is running, creating interactive computing
  Response time should be < 1 second
  Each user has at least one program executing in memory process
  If several jobs ready to run at the same time  CPU scheduling
  If processes don’t fit in memory, swapping moves them in and out to run
  Virtual memory allows execution of processes not completely in memory

## Slide 40: Memory Layout for Multiprogrammed System

## Slide 41: Chapter 1: Introduction
What Operating Systems Do
Computer-System Organization
Computer-System Architecture
Operating-System Structure
Operating-System Operations
Process Management
Memory Management
Storage Management
Protection and Security
Kernel Data Structure
Computing Environments
Open-Source Operating Systems

## Slide 42: Operating-System Operations
Interrupt driven by hardware
Software error or request creates exception or trap
  Division by zero, request for operating system service
Other process problems include infinite loop, processes modifying each other or the OS
Dual-mode operation allows OS to protect itself and other system components
  User mode and kernel mode
  Mode bit provided by hardware
    Provides ability to distinguish when system is running user code or kernel code
    Some instructions designated as privileged, only executable in kernel mode
    System call changes mode to kernel, return from call resets it to user

## Slide 43: Transition from User to Kernel Mode
Timer to prevent infinite loop / process hogging resources
  Set interrupt after specific period
  Operating system decrements counter
  When counter zero generates an interrupt
  Set up before scheduling process to regain control or terminate program that exceeds allotted time

## Slide 44: Chapter 1: Introduction
What Operating Systems Do
Computer-System Organization
Computer-System Architecture
Operating-System Structure
Operating-System Operations
Process Management
Memory Management
Storage Management
Protection and Security
Kernel Data Structure
Computing Environments
Open-Source Operating Systems

## Slide 45: Process Management
A process is a program in execution. It is a unit of work within the system.
Program is a passive entity, process is an active entity.
Process needs resources to accomplish its task
  CPU, memory, I/O, files
  Initialization data
Process termination requires reclaim of any reusable resources
Single-threaded process has one program counter specifying location of next instruction to execute
  Process executes instructions sequentially, one at a time, until completion
Multi-threaded process has one program counter per thread
Typically system has many processes, some user, some operating system running concurrently on one or more CPUs
  Concurrency by multiplexing the CPUs among the processes / threads

## Slide 46: Process Management Activities
The operating system is responsible for the following activities in connection with process management:
  Creating and deleting both user and system processes
  Suspending and resuming processes
  Providing mechanisms for process synchronization
  Providing mechanisms for process communication
  Providing mechanisms for deadlock handling

## Slide 47: Chapter 1: Introduction
What Operating Systems Do
Computer-System Organization
Computer-System Architecture
Operating-System Structure
Operating-System Operations
Process Management
Memory Management
Storage Management
Protection and Security
Kernel Data Structure
Computing Environments
Open-Source Operating Systems

## Slide 48: Memory Management
All data in memory before and after processing
All instructions in memory in order to execute
Memory management determines what is in memory when
  Optimizing CPU utilization and computer response to users
Memory management activities
  Keeping track of which parts of memory are currently being used and by whom
  Deciding which processes (or parts thereof) and data to move into and out of memory
  Allocating and deallocating memory space as needed

## Slide 49: Chapter 1: Introduction
What Operating Systems Do
Computer-System Organization
Computer-System Architecture
Operating-System Structure
Operating-System Operations
Process Management
Memory Management
Storage Management
Protection and Security
Kernel Data Structure
Computing Environments
Open-Source Operating Systems

## Slide 50: Storage Management
OS provides uniform, logical view of information storage
  Abstracts physical properties to logical storage unit - file
  Each medium is controlled by device (i.e., disk drive, tape drive)
    Varying properties include access speed, capacity, data-transfer rate, access method (sequential or random)
File-System management
  Files usually organized into directories
  Access control on most systems to determine who can access what
  OS activities include
    Creating and deleting files and directories
    Primitives to manipulate files and dirs
    Mapping files onto secondary storage
    Backup files onto stable (non-volatile) storage media

## Slide 51: Mass-Storage Management
Usually disks used to store data that does not fit in main memory or data that must be kept for a “long” period of time.
Proper management is of central importance
Entire speed of computer operation hinges on disk subsystem and its algorithms
OS activities
  Free-space management
  Storage allocation
  Disk scheduling
Some storage need not be fast
  Tertiary storage includes optical storage, magnetic tape
  Still must be managed
  Varies between WORM (write-once, read-many-times) and RW (read-write)

## Slide 52: I/O Subsystem
One purpose of OS is to hide peculiarities of hardware devices from the user
I/O subsystem responsible for
  Memory management of I/O including buffering (storing data temporarily while it is being transferred), caching (storing parts of data in faster storage for performance), spooling (the overlapping of output of one job with input of other jobs)
  General device-driver interface
  Drivers for specific hardware devices

## Slide 53: Chapter 1: Introduction
What Operating Systems Do
Computer-System Organization
Computer-System Architecture
Operating-System Structure
Operating-System Operations
Process Management
Memory Management
Storage Management
Protection and Security
Kernel Data Structure
Computing Environments
Open-Source Operating Systems

## Slide 54: Protection and Security
Protection – any mechanism for controlling access of processes or users to resources defined by the OS
Security – defense of the system against internal and external attacks
  Huge range, including denial-of-service, worms, viruses, identity theft, theft of service
Systems generally first distinguish among users, to determine who can do what
  User identities (user IDs, security IDs) include name and associated number, one per user
  User ID then associated with all files, processes of that user to determine access control
  Group identifier (group ID) allows set of users to be defined and controls managed, then also associated with each process, file
  Privilege escalation allows user to change to effective ID with more rights

## Slide 55: Chapter 1: Introduction
What Operating Systems Do
Computer-System Organization
Computer-System Architecture
Operating-System Structure
Operating-System Operations
Process Management
Memory Management
Storage Management
Protection and Security
Kernel Data Structure
Computing Environments
Open-Source Operating Systems

## Slide 56: Kernel Data Structure
Lists, Stacks, and Queues
Trees
Hash Functions and Maps
Bitmaps
<linux/list.h>

## Slide 57: Chapter 1: Introduction
What Operating Systems Do
Computer-System Organization
Computer-System Architecture
Operating-System Structure
Operating-System Operations
Process Management
Memory Management
Storage Management
Protection and Security
Kernel Data Structure
Computing Environments
Open-Source Operating Systems

## Slide 58: Computing Environments (1/2)
Traditional computer
  Blurring over time
  Office environment
    PCs connected to a network, terminals attached to mainframe or minicomputers providing batch and timesharing
    Now portals allowing networked and remote systems access to same resources
  Home networks
    Used to be single system, then modems
    Now firewalled, networked

## Slide 59: Computing Environments (2/2)
Client-Server Computing
  Dumb terminals supplanted by smart PCs
  Many systems now servers, responding to requests generated by clients
    Compute-server provides an interface to client to request services (i.e. database)
    File-server provides interface for clients to store and retrieve files

## Slide 60: Peer-to-Peer Computing
Another model of distributed system
P2P does not distinguish clients and servers
  Instead all nodes are considered peers
  May each act as client, server or both
  Node must join P2P network
    Registers its service with central lookup service on network, or
    Broadcast request for service and respond to requests for service via discovery protocol
  Examples include Napster and Gnutella

## Slide 61: Web-Based Computing
Web has become ubiquitous
PCs most prevalent devices
More devices becoming networked to allow web access
New category of devices to manage web traffic among similar servers: load balancers
Use of operating systems like Windows 95, client-side, have evolved into Linux and Windows XP, which can be clients and servers

## Slide 62: Chapter 1: Introduction
What Operating Systems Do
Computer-System Organization
Computer-System Architecture
Operating-System Structure
Operating-System Operations
Process Management
Memory Management
Storage Management
Protection and Security
Distributed Systems
Special-Purpose Systems
Computing Environments
Open-Source Operating Systems

## Slide 63: Open-Source Operating Systems
Closed-source OS
Reverse engineering
Copyright, copyleft
Digital Rights Management (DRM)
Free Software Foundation (FSF)
GNU General Public License (GPL)
Linux 2.6.x, 3.x, BSD UNIX, Solaris
Utility, open-source projects

## Slide 64: Categories of free and nonfree software

## Slide 65: Chapter 1: Introduction
What Operating Systems Do
Computer-System Organization
Computer-System Architecture
Operating-System Structure
Operating-System Operations
Process Management
Memory Management
Storage Management
Protection and Security
Distributed Systems
Special-Purpose Systems
Computing Environments
Open-Source Operating Systems

## Slide 66: Distributed Systems
LAN
  local-area network
WAN
  wide-area network
MAN
  metropolitan-area network
SAN
  small-area network
NOS
  Network operating system
DOS
  Distributed operating system

## Slide 67: Chapter 1: Introduction
What Operating Systems Do
Computer-System Organization
Computer-System Architecture
Operating-System Structure
Operating-System Operations
Process Management
Memory Management
Storage Management
Protection and Security
Distributed Systems
Special-Purpose Systems
Computing Environments
Open-Source Operating Systems

## Slide 68: Special-Purpose Systems
Real-Time Embedded Systems
  Embedded systems almost always run real-time operating systems?
Multimedia Systems
Handheld Systems

## Slide 69: End of Chapter 1